## Slide 1: A mid-infrared PI Instrument for Subaru
Takafumi Kamizuka (P.D @ IoA/UT)
MIMIZUKU Development Team

## Slide 2: About MIMIZUKU
MIMIZUKU = Mid-Infrared Multi-field Imager for
gaZing at the UnKnown Universe
1st-gen. instrument for TAO 6.5-m telescope
Unique Capability of MIMIZUKU
Wide Band Coverage
  2—26 μm (for Subaru)
  2—38 µm (for TAO)
High-Precision Observation
  Utilizing “Field Stacker” Device
High Spatial Resolution
  0.3”/0.6” @ 10/20μm
  1” @ 30μm available at TAO
MIMIZUKU (2m x 2m x 2m; 2.4t)

## Slide 3: Development Team
Institute of Astronomy, UT
  Takashi MIYATA (P.I.; Assoc. Prof.)
  Shigeyuki SAKO (Assist. Prof.)
  Takafumi KAMIZUKA (P.D.)
  Kentaro ASANO (D3)
  Mizuho UCHIYAMA (D2)
  Kazushi OKADA (M2)
Department of Astronomy, UT
  Takashi ONAKA (Prof.)
  Itsuki SAKON (Assist. Prof.)
  Tomohiko NAKAMURA (P.D.)
Institute of Space and Astronautical Science, JAXA
  Hirokazu KATAZA (Assoc. Prof.)
Subaru Telescope, NAOJ
  Takuya FUJIYOSHI (Sr. Resident Astronomer)

## Slide 4: Capabilities of MIMIZUKU Wide Band Coverage
λ = 2—38 µm is covered by 3 Cameras
with capability of Imaging and Spectroscopy
 |  | NIR | MIR-S | MIR-L
Wavelength |  | 2—6μm | 6—26μm | 24—38μm
Detector |  | Teledyne H1RG HgCdTe 1kx1k | Raytheon Aquarius Si:As 1kx1k | DRS HF-128 Si:Sb 128x128
Pixel Scale |  | 0.052”/pix | 0.087”/pix | 0.18”/pix
FoV | w/ FS | 0.9’ x 0.9’ | 1.5’ x 1.5’ | 0.4’ x 0.4’
 | w/o FS | 0.9’ x 0.4’ x 2 fields | 1.5’ x 0.7’ x 2 fields | 0.4’ x 0.2’ x 2 fields
Img. Filter |  | L’, M J, H, K | N-band (R~10) x 4 Q-band (R~20) x 2 Narrow-band (Δλ~0.2μm) | 31μm (R~10) 35μm (R~10) 37μm (R~10)
Spectroscopy |  | 2.8—5.5μm R~180 | 7.5—13.5μm R~230 16.5—25.5μm R~160 | 26—38μm R~70
Slit |  | 0.3”x60” | 0.3”/0.6” x 60” | 1.2”x50”
Gray letter means Optional
Specifications of MIMZIUKU
Some specs are slightly
modified from proposal

## Slide 5: Capabilities of MIMIZUKU High Precision Observation
“Field Stacker” enables real-time calibration,
which is free from atmospheric time variation
 Precise Photometry/Spectroscopy
Field Stacker
φ 5’ (Subaru)
Target and Std. obj. are observed simultaneously
Precise Calibration
Long-term monitoring
Reliable Spectroscopy
Installed here!
Schematic view of Field Stacker

## Slide 6: Capabilities of MIMIZUKU High Spatial Resolution
Diffraction limited image at λ > 8μm
Resolution of NIR camera is ~ 0.2”
Subaru 8.2m telescope gives us the highest spatial resolution at MIR.
At 30μm band, MIMIZUKU will achieve the highest spatial resolution
(mainly for TAO)
Spatial resolution of recent MIR instruments

## Slide 7: Science Case
Origin of Terrestrial Material
from dying stars to aborning earths
Supernovae
Planetary nebulae
Dying Stars
Destroyed?
Interstellar
Protoplanetary
Disk
Planetesimal
Primordial bodies
Earth
Modified?
Modified?
From dying stars to aborning earths
The history is recorded
in small grains…
?
?
?
?
Formed & Modified?

## Slide 8: Science Case
We want to propose an intensive / strategic program to monitor these objects.
~20 targets
1-2 runs / semester
~3 semesters
MIMIZUKU Monitoring Program
Missing Iron Grains (AGBs)
Dust Stream in Protoplanetary Disks (PPDs)
Giant Impacts on Young Exoplanets (Debris Disks)
Fresh Dust in Explosions (SNe/Novae)
Follow-up of Space Missions (Solar system)
In addition …
  MIMIZUKU Science Workshop
  was held on 2013/5/24
  ~40 scientists attended
  ~15 talks were presented

## Slide 9: Development
Motion test of F/S is successfully done
Switch board is completed
Improving cooling capability of Cryostat
Cryostat & F/S will be completed in the early 2014
Optics is fabricated
Degradation of mirrors occurred (galvanic corrosion)
Re-fabrication is ongoing
  SiO coating will be applied to avoid the degradation
Re-fabrication will be done in the early 2014.
Cryostat & Field Stacker
Optics
Field Stacker
Up & down motion test
Cryostat
Switch Board
Cold Optics
Damaged mirror

## Slide 10: Development
Fabrication is almost done
Black painting is being applied
Cryogenic motion test is ongoing
Control programs are being developed
These will be completed until the middle of 2014
Aquarius is already purchased
H1RG and Si:Sb HF-128 are coming soon
Digital boards are completed
Analog boards are under development
Detector drive system will be completed in the middle of 2014.
Cryogenic Drive System
Detector System
Cryogenic Drive Units
(Filter wheel etc.)
Cryogenic motor test
Fabricated Board

## Slide 11: Schedule
FY2014
FY2015
FY2016
FY2017
FY2018
FY2019
Cryostat & F/S
Optics
Cryo. Driv. Sys.
Detector
Control System
Total Test
To Hawaii
Test
PV Obs.
Open Use
To Chile
Test & Obs.
Construction of TAO

## Slide 12: Summary
Development of MIMIZUKU is going on to realize precise monitoring observation for investigating the origin and evolution of cosmic dust.
The development will be completed at the end of FY 2014.
Then, MIMIZUKU will be transferred to Hawaii.
MIMIZUKU will be available for open-use programs
from 2016A to 2017B.
MIMIZUKU will be transferred to Chile after the completion of TAO around 2018.
Visit our HP : http://www.ioa.s.u-tokyo.ac.jp/TAO/mimizuku/pub/

## Slide 14
Excess = Iron grains?
Water vapor?
1
10
1
0.1
Fνλ2 (Jy/μm2)
Photosphere
(McDonald et al. 2010)
Wavelength (μm)
10

## Slide 15
L = 50Lo
L = 120Lo
Vinkovic 2009
Trajectory of dust grain
amorphous
crystalline
+
amorphous
Circumstellar disk
quiescence
outburst
2005/3
2008/4
Example of EX Lupi
Abraham+ 2009

## Slide 16
Debris disk HD172555
Silica
Silica
spaceref.com

## Slide 17: Science Case
We want to propose an intensive / strategic program to monitor these objects.
~20 targets
1-2 runs / semester
~3 semesters
MIMIZUKU Monitoring Program
Missing Iron Grains (AGBs)
Dust Stream in Protoplanetary Disks (PPDs)
Giant Impacts on Young Exoplanets (PPDs)
Fresh Dust in Explosions (SNe/Novae)
Follow-up of Space Missions (Solar system)
In addition …
  MIMIZUKU Science Workshop
  was held on 2013/5/24
  ~40 scientists attended and
  ~15 talks were presented