## Slide 1
Next generation wide field AO (GLAO) and NIRMOS for Subaru Telescope.
Ultra-wide-field
Laser
Tomographic
Imager and
MOS with
AO for
Transcendent
Exploration
by
SUBARU telescope.

## Slide 2: Adaptive Telescope
Adaptive
Scondary
Mirror
Wavefront
Sensor
NIR instrument
4 laser guide star

## Slide 3
Atmospheric
turbulence
Wavefront
sensors
Feedback correction
to deformable
secondary mirror
Turbulence at
ground layer
Estimation of
ground-layer turbulence
Guide stars

## Slide 4: GLAO - Specifications under Consideration
Guide stars | 4 LGSs + 3 NGSs | 
DM | Secondary mirror | ~1000 actuators, modification of VLT ASM.
HO-WFS | > 8x8 SH | visible, EM-CCD(TBD)
TT(F)-WFS | 2x2 SH or quad | visible
Laser | 20 W CW | TOPTICA (589nm) (option: Rayleigh)
LGS constellation | 15’ in diameter | 
Laser Launch | ~25cm dia. (TBD) | side launch

## Slide 5: NIR Instrument - Specifications under Consideration
Wavelength | 0.8-2.5μm | 
Plate Scale | 0.06-0.1”/pix | 
FoV | approx.13‘x13’ | Wider with Split FoVs?
Filters | Broad+Narrow | R?, I,z,J,H,K, NB
MOS | Multi Slit Mask | Alternatively Multi-IFU
λ Dispersion | 2000(TBD) | Under Investigation

## Slide 6: Comparison: Imaging
 | Subaru MOIRCS | Subaru GLAO | TMT IRIS | HST WFC3/IR | JWST NIRCam
Telescope Aperture | 8.2m | 8.2m | 30m | 2.4m | 6.5m
Wavelength Coverage | 0.9-2.5μm | 0.9-2.5μm | 0.84-2.4μm | 0.9-1.7μm | 0.9-2.3μm / 2.4-5.0μm
Spatial Resolution | 0.117”/pix 0.4”@2μm | ~0.1”/pix 0.2”@2μm | 4 mas 10mas@1μm | 0.13”/pix FWHM~ 0.25” | 32 mas / 64 mas
Field of View | 28 □’ | ~180 □’ | 0.075 □’ | 4.65 □’ | 9.7 □’

## Slide 7: Comparison: Spectroscopy
 | Subaru MOIRCS | Subaru GLAO | TMT IRIS | HST WFC3/IR | JWST NIRSpec
Wavelength Coverage | 0.9-2.5μm | 0.9-2.5μm | 0.84-2.4μm | 0.9-1.7μm | 0.6-5μm
Spatial Resolution | 0.117”/pix 0.4”@2μm | ~0.1”/pix 0.2”@2μm | 4 - 50 mas | 0.13”/pix FWHM~ 0.25” | 0.2”x0.45”
Field of View | ~25 □’ | ~120 □’ | 0.2-10 □” | 4.65 □’ | 12.24 □’(MSA) 3”x3”(IFS)
Functions | Single-Slit MOS IFS | MOS Multi-IFS? | IFS | Slitless | Slits Microshutters IFS
Spectral Resolution | 600-3000 | -2000? | 4000-10000 | TBW | 100, 1000, 2700

## Slide 8: Perfoamance simulation
Add to match seeing statistics at Subaru.
TMT site test at 13N
Turbulence profile
GS asterism
 | R | J | H | K
Seeing | 0.65” | 0.51” | 0.49” | 0.44”
GLAO | 0.41” | 0.27” | 0.23” | 0.20”
FWHM
 | R | J | H | K
Seeing | 9% | 12% | 15% | 17%
GLAO | 16% | 29% | 36% | 41%
Ensquared Energy (0.24”x0.24”)
 | 0° | 15° | 30° | 45° | 60°
Seeing | 0.44” | 0.49” | 0.52” | 0.60” | 0.76”
GLAO | 0.20” | 0.28” | 0.31” | 0.38” | 0.55”
Zenith angle dependency
S. Oya

## Slide 9: Sky coverage
Dash circle line: 7.5’ radius
★:LGS
●: TTFGS
Searching area for TTFGS
D. Simons, Gemini technical notes TN-PS-G0030, (1995).
r(in, out) = r_circ | TTFGS(R-band) | b: 10~20 deg | 30~50 deg | 60~90 deg | 
(7' ,8') = 1.6' | < 18 mag | > 6.7 | > 3.0 | > 1.8 | 
 | < 19 mag | > 10.7 | > 4.8 | > 2.8 | 1 mag fainter
(7', 8.5') = 2.0' | < 18mag | > 34.7 | > 7.4 | > 4.3 | 1‘ dia. wider
S. Oya
Notes: 18mag: 34.1670 13.1761 6.7217 4.2019 3.0303 2.3584 1.9951 1.7573 1.7562
19mag: 65.2393 21.7403 10.6814 6.6279 4.7669 3.7023 3.1285 2.7500 2.7500
17': 101.1209 33.6974 16.5562 10.2732 7.3887 5.7385 4.8492 4.2625 4.2625
In .conf: 800Hz & effectively half for EM-CCD, i.e. actually x8
LGS(32x32SA): 10mag ⇒ 33.597 x 8 = 268.776
TTF(4SA): 18mag ⇒ => 5.397 x 8 = 43.1760
9

## Slide 10: Conceptual study
Performance simulation update
Deformable secondary mirror
Laser system
Telescope interface and modification
Optical design of NIR instrument

## Slide 11: Preliminary model for ASM
Mirror Dia: 1265mm
Actuators: 924
Spacing: ~ 35 mm
Center obscuration:
350mm

## Slide 12: Interface to existing IR M2

## Slide 13: Vignetting by telescope structures
Cassegrain Unit
M3 Unit
M1 cell
cover

## Slide 14: Cassegrain Unit
Remove
Remove
Modify
① ADC
Remove
φ16 arcmin

## Slide 15: M3 unit
φ16 arcmin

## Slide 16: Wide-Field NIR Imager+Multi-Object Spectrograph (A case without FoV splitting)
Optical Design by Dr. Yamamuro (Optcraft)
FoV 12.6’
input window
field flattener
collimating lenses
focusing lenses

## Slide 17: Project preparation
Project organization
  PI (Nobuo Arimoto, Director of Subaru Telescope.)
  Project management (Hayano)
  Project AO scientist (Oya, Lai)
  Project scientist (Kodama, Iwata, Minowa)
International collaborators
  Gemini, HIA, ASIAA etc.

## Slide 18: Project organization
Primary Investigator
N. Arimoto
Project Management
Y. Hayano
T. Kodama
O. Lai
I.Iwata
S. Oya
Y. Minowa

## Slide 19: Schedule
2012
13
14
15
16
17
18
19
2020
Concept Design
Prelim Design
Detail Design
Fabrication
Telescope Modification
Integration and Test
Science Operation
Review
FL
TMT
PFS
HSC
AO188/LGS
Review
Review

## Slide 20: Feasible schedule (plan)
Upgrade to Adaptive Telescope
  Adaptive Secondary Mirror.
    Grant-in-Aid, Specially Promoted Research, (Tokubetu-shuishin), 2014 or 2015, 5 years,
  Wavefront sensor and lasers.
    Grant-in-Aid, New research field, (Shin-gakujutu), 2014 or 2015, 5 years.
    Collaboration with biology researcher.
  GLAO + Nu MOIRCS
NIR wide field instrument.
  Imager, MOS or M-IFS.
  International collaboration or other Grant-in-Aid.

## Slide 21: Cost Estimation
Item | Cost (USD)
Adaptive Secondary Mirror | 5-10M
Laser System | 4-8M
Wavefront Sensor System | ~3.5M
Computers | ~0.2M
Telescope Modifications | 15-20M
Instruments | 5-20M
(Additional) Human Resources | ~2M
Total | 35-60M