## Slide 1: NIR Instrument for GLAO
Takashi Hattori, Iwata Ikuru (Subaru Telescope)

## Slide 2: Instrument for GLAO
Need for wide field NIR instrument
  GLAO : good image quality over 15’ FoV
  cf. current Cs NIR instrument (MOIRCS) has 4’ x 7’ FoV
Three Candidates
  Wide-Field Imager
    conceptual study by Dr. John Pazder (HIA)
  Wide-Field Imager and Multi-Object Spectrograph
    optical designs by OptCraft
  Multi-Object Integral Field Spectrograph
    KMOS-like instrument?

## Slide 3: Modifications to the Telescope
original design of the telescope : Φ6’ FoV for Cs
  modifications are necessary for wider FoV
  may affect the plan of the new instrument
study by MELCO
  FoV up to Φ20’ at Cs
  vignettings by telescope structures : Cassegrain-unit, M3-unit, and Cell-cover

## Slide 4: Vignettings by Telescope Structure
M3-unit
Cs-unit
Cell-cover
MELCO (2013)
(top view)

## Slide 5: Vignettings by Telescope Structure
4.9mm
15.2mm
Light Path
14’ FoV
  M3-unit
    2 small overlaps
    only small modifications
    are necessary
MELCO (2013)

## Slide 6: Vignettings by Telescope Structure
14’ FoV
  Cs-unit
    ADC, AG/SH, CAL, and SV are need to be removed and implemented to the new instrument if necessary
MELCO (2013)

## Slide 7: Vignettings by Telescope Structure
14’ FoV
  Cell-cover
    has to be removed/replaced for FoV > Φ12’
Light Path
(Φ14’)
MELCO (2013)

## Slide 8: Vignettings by Telescope Structure
20’ FoV
  most structures of M3-unit overlap Φ20’ light path
  new development of M3-unit is necessary
MELCO (2013)

## Slide 9: Modifications to the Telescope
Summary
  ≦Φ12’
    remove/replace ADC, AG/SH, CAL, and SV in Cs-unit
  Φ14’
    remove/replace cell-cover
    small modifications to M3-unit
  Φ20’
    new development of M3-unit
      significant modification to the telescope
    need more study

## Slide 10: (1) Wide Field NIR Imager
conceptual study by Dr. John Pazder (HIA)
concentric corrector + 4-barrel imaging system
Pazder (2013)

## Slide 11: (1) Wide Field NIR Imager
concentric corrector
  universal GLAO focus station (22’.8 FoV)
  image quality < 66mas at the telescope focus
require significant modification to the telescope
Pazder (2013)

## Slide 12: (1) Wide Field NIR Imager
imaging system
  each camera covers 6’.8x6’.8
    0”.1 sampling with one H4RG-15
  image quality at the detector
  < 1pixel (except at the outer corner, rms diameter~16μm)
Pazder (2013)

## Slide 13: (1) Wide Field NIR Imager
specifications
Wavelength | 0.8-2.5μm
Pixel Scale | 0”.1 / pixel
FoV | 6’.8x6’.8x4 (185□’)
Detectors | H4RG x 4
Filters | Broad + Narrow

## Slide 14: (2) Wide Field NIR Imager and MOS
optical designs by OptCraft
  with/without FoV splitting
  with/without change in M2 parameters (and M1 deformation)
  optical components (CaF2) < 400mm
  image quality < 0”.15 in 0.8-2.5μm (goal)
  flat focal plane for MOS
MOS mask exchanger, narrow-band filter
  need studies

## Slide 15: (2) Wide Field NIR Imager and MOS
single FoV, no-change to M2 parameters
FoV Φ12’.6
OptCraft (2012)

## Slide 16: (2) Wide Field NIR Imager and MOS
single FoV, no-change to M2 parameters (imaging)
  image quality <0”.15 rms except for 800-900nm (<0”.18)
100μm
=0”.53
OptCraft (2012)

## Slide 17: (2) Wide Field NIR Imager and MOS
specifications under consideration
Wavelength | 0.8-2.5μm
Pixel Scale | 0”.06 – 0”.1 / pixel
Detectors | H4RG x 4
Filters | Broad + Narrow
MOS | Multi Slit Mask
Dispersion | R=2000-3000

## Slide 18: (2) Wide Field NIR Imager and MOS
spatial sampling and FoV
Pixel Scale | FoV for 4 H4RGs
0.06 | 8’.19
0.07 | 9’.56
0.08 | 10’.92
0.09 | 12’.29
0.10 | 13’.65

## Slide 19: (2) Wide Field NIR Imager and MOS
A case with FoV splitting
    require significant modifications to the telescope
AO Guide Star
pick-off area
4 H4RG
0.06”/pix
OptCraft (2013)
~23’

## Slide 20: (2) Wide Field NIR Imager and MOS
A case with FoV splitting
OptCraft (2013)
(1 of the four FoVs)

## Slide 21: (2) Wide Field NIR Imager and MOS
grism performance study by Photocoding
  ZnSe or Si grisms for R=3000-3500
mechanical feasibility study by SHI
  the case with FoV splitting
  ongoing

## Slide 22: (3) Multi-Object Integral Field Spectrograph
no specific study so far
instrument similar to KMOS (VLT)
KMOS

## Slide 23: (3) Multi-Object Integral Field Spectrograph
specifications under consideration
Wavelength | 0.8-2.5μm
Pixel Scale | 0”.15 / pixel
Number of IFU | 24
FoV/IFU | 1”.8 x 1”.8
Patrol Area | 13-16’ ?
Dispersion | R=2000-3000 ?

## Slide 24: Three Levels of Instrument Plan for GLAO
(0) No new instrument – use MOIRCS
(1) Wide-field NIR Imager
(2) Wide-field NIR Imager + MOS (WFNIRMOS)
(3) Multi-object Integral Field Spectrograph
・Which instrument is essentially important for your
science cases?
・What is the optimal sampling/FoV for your science
cases?

## Slide 25: Spatial sampling vs. FoV
NIR Imager or Imager+MOS
Pixel Scale | FoV for 4 H4RGs
0.06 | 8’.19
0.07 | 9’.56
0.08 | 10’.92
0.09 | 12’.29
0.10 | 13’.65