## Slide 1: Ultra-wide-field Laser Tomographic Imager and MOS with AO for Transcendent Exploration by SUBARU telescope.
PI: N. Arimito
PM: Y. Hayano
PS: T. Kodama

## Slide 2: Project overview
Why we need ULTIMATE-SUBARU?
GLAO System overview
Seeing at Mauna Kea (next talk by Oya-san)
GLAO simulation (next talk by Oya-san)
Project organization
Schedule and budget
Technical studies
  Adaptive secondary mirror study
  Telescope modification study
  Wide field imager

## Slide 3: Key instruments at Subaru Telescope 鼎（tripod pot）
HSC
(vis)
PFS
(vis)
GLAO
NIR instrument
HSC first light

## Slide 4: System Overview
Adaptive
Scondary
Mirror
Wavefront
Sensor
NIR instrument
4 laser guide star
Ground Layer AO with Adaptive Secondary Mirror (4 LGSs)
Wide-field Near-IR Instrument (Imager + MOS or M-IFU)
→ Seeing Improvement (FWHM 0.4”→0.2”) over FOV ~15’
    Higher Sensitivity Equivalent to 2x Telescope Aperture*1
    6 Times Wider Field of View*2
Targeted to Start Commissioning in 2020
*1 For point sources.
*2 Relative to MOIRCS (seeing limited NIR instrument)

## Slide 5: GLAO
Atmospheric
turbulence
Wavefront
sensors
Feedback correction
to deformable
secondary mirror
Turbulence at
ground layer
Estimation of
ground-layer turbulence
Guide stars

## Slide 6: System Overview
Adaptive
Scondary
Mirror
Wavefront
Sensor
NIR instrument
4 laser guide star
Ground Layer AO with Adaptive Secondary Mirror (4 LGSs)
Wide-field Near-IR Instrument (Imager + MOS or M-IFU)
→ Seeing improvement (FWHM 0.4”→0.2”) over FOV ~15’
    Higher sensitivity equivalent to 2x telescope aperture*1
    6 times wider FOV*2
      ~200 times wider FOV compared with AO188/LGS+IRCS
Targeted to Start Commissioning in 2020
*1 For point sources.
*2 Relative to MOIRCS (seeing limited NIR instrument)

## Slide 7: GLAO - Specifications under Consideration
Guide stars | 4 LGSs + 3 NGSs | 
DM | Secondary mirror | ~1000 actuators, modification of VLT ASM.
High-order WFS | > 8x8 SH | visible, EM-CCD(TBD)
Tip-tilt-focus WFS | 2x2 SH or quad | visible
Laser | 20 W CW | TOPTICA (589nm) (option: Rayleigh)
LGS constellation | 15’ in diameter | 
Laser Launch | ~25cm dia. (TBD) | side launch

## Slide 8: NIR Instrument - Specifications under Consideration
Wavelength | 0.8-2.5μm | 
Plate Scale | 0.06-0.1”/pix | 
FoV | approx.13‘x13’ | Wider with Split FoVs?
Filters | Broad+Narrow | R?, I,z,J,H,K, NB
MOS | Multi Slit Mask | Alternatively Multi-IFU
λ Dispersion | 2000(TBD) | Under Investigation

## Slide 9: Main Science Targets
“Anatomy” of galaxies at z=1 – 3
  What are the key parameters to drive the galaxy evolution?
  What determines morphologies of the galaxies?
  Large-Scale Near-IR Surveys (Imaging and spectroscopy) of about 5000 galaxies
Discovery of the Most Distant Galaxies at z>7.5
  Understand of the Cosmic Reionization
  NBF imaging survey (〜180 arcmin2), 100 galaxies.
  → Target sample for TMT.

## Slide 10
PI
N. Arimito
Subaru Director
Project management
Y. Hayano、O. Lai
Science team
T. Kodama、I. Iwata.
ngAO working group menbers
International collaborators
ULTIMATE-SUBARU organization
Adaptive Optics
2nd DM (Adoptica, MELCO, NAOJ)
WFS (NAOJ, others）
LGS (TOPTICA, NAOJ, others)
RTC (NAOJ, others）
Telescope Mod. (MELCO, NAOJ)
Test and Integration（NAOJ, etc）
Opto-mechanics (NAOJ, coll.）
Electronics(NAOJ, coll.）
Control (NAOJ, coll.）
Software(NAOJ, coll.）
Staff 3/Postdoc 3/Tech 2/coll.
Wide-field NIR inst.
Opto-mechanics (NAOJ, coll.）
Electronics(NAOJ, coll.）
Cryogenic system(NAOJ, coll.）
Detector, Camera(NAOJ, coll.）
Control(NAOJ, coll.）
Data analysis(NAOJ, coll.）
Staff 3/Postdoc 3/Tech 2/Coll.

## Slide 11: Schedule
2012
13
14
15
16
17
18
19
2020
Concept Design
Prelim Design
Detail Design
Fabrication
Telescope Modification
Integration and Test
Science Operation
Review
FL
TMT
PFS
HSC
AO188/LGS
Review
Review

## Slide 12
Items | Cost | Budget
ASM system | 6 M | Grant-in-aid Scientific Research, etc.
Laser system | 0.5 – 4 M | Grant-in-aid Scientific Research, etc. (if Rayleight LGSs, cost is 1/10)
Wavefront sensor unit | 1 M | Grant-in-aid Scientific Research (International collaboration)
Realtime controller | 0.5 M | Grant-in-aid Scientific Research, etc. (International collaboration)
Telescope modification | 5 – 8 M | NAOJ budget
NIR instrument | 0 – 10 M | Existing instrument at first. (MOIRCS or MOIRCS upgrade etc.)
Manpower | 2 M | NAOJ budget and Grant-in-aid Scientific Research
Contingency | 5 M | 
Total | 20 – 36.5 M | 
Cost estimation, budget
Grant-in-Aid for Scientific Research on Innovative Areas, 2015-2019
Grant-in-Aid for Specially Promoted Research, 2016-2020
Grant-in-Aid for Scientific Research (Category S), 2020-2024

## Slide 13: Technical studies

## Slide 14
Thin shell mirror
Thin shell supporting foam
Reference plate
Actuators
Actuator plate
Control electronics
Interface cables
(Power, Network, coolant)
Hexapods will be located around control electronics.
Adaptive Secondary mirror for VLT

## Slide 15: ASM test unit at ESO (ASSIST) (2012/11/13)

## Slide 16: ASM test at ESO with GRALL (2013/3/27)

## Slide 18: Subaru ASM model

## Slide 20: Interface to existing IR M2

## Slide 21: Vignetting by telescope structures
Cassegrain Unit
M3 Unit
M1 cell
cover

## Slide 22: Cassegrain Unit
Remove
Remove
Modify
① ADC
Remove
φ16 arcmin

## Slide 23: FOV at Cassegrain (current)

## Slide 24: M3 unit
φ16 arcmin

## Slide 25: Expandable FoV at Cassegrain
Only M1, M2
With M3 unit
~ 8’

## Slide 26: Location of LLT and laser head
Rear
Front
OPT
IR
Balance weight
Balance weight
No longer exist
Cable wrap and duct at elevation axis (IR)
Cable wrap and duct at elevation axis (OPT)
Winch for mirror cover
Walk way
Cable tray area (Use during M1 coating)
Terminal box (lower center section)
Candidate location

## Slide 27: Candidate location for LLT

## Slide 28: Front side
Laser head and
LLT location

## Slide 29: Rear side
Laser head and
LLT location

## Slide 30: Feasibility study for NIR instrument
Optical design
  w/wo field splitting
  Change telescope optical parameters or not.
  Optical components (CaF2) < 400mm
  Goal FWHM <0.15” over FoV and 0.8-2.5μm

## Slide 31: Wide-Field NIR Imager+Multi-Object Spectrograph (A case without FoV splitting)
Example of Optical Design
FoV 12.6’
input window
field flattener
collimating lenses
focusing lenses

## Slide 32: Next step
Conceptual design review
International Collaboration
  AAO、NRC, etc.
Adaptive secondary mirror
  Interface to IR M2 unit.
  Further design study with ADS, Microgate.
Fiber laser (TOPTICA/MPBC) upgrade
Budget application
  Grant-in-Aid for Scientific Research on Innovative Areas, 2015-2019.