## Slide 1: 東京大学が進める光赤外線分野の 基礎開発研究
東京大学 天文学教育研究センター
Institute of Astronomy, the University of Tokyo
酒向 重行 (SAKO, Shigeyuki)
2011/1/18 すばる将来装置計画ワークショップ 国立天文台
Basic developments on optical-infrared astronomy
driven by the University of Tokyo

## Slide 3: Framework of developments in U-Tokyo
TAO
miniTAO
Mitaka(IoA)
Hongo
KISO
Headquarter in Tokyo
Observatory in Atacama, Chile
Oversea base
Observatory in Kiso, Japan
Domestic base
6.5-m telescope (future plan)
1.0-m telescope
1.0-m telescope
Developments of instruments and basic technologies are mainly proceeding at Mitaka and Kiso.
Staff: 14†
TS : 1
PD : 3†
ST :25(16)
Staff: 0
TS : 3
PD : 2
ST : 0
Staff: 0
TS : 0
PD : 0
ST : 0
Staff: 9†
TS : 0
PD : 1†
ST:15(9)
† Including persons on other research fields

## Slide 4: Instruments developed by U-Tokyo
Development phase
Observation phase
List of instruments whose PI is in U-Tokyo
for TAO 6.5-m and Subaru 8.2-m | SWIMS | NIR camera and spec. with MOS
 | MIMIZUKU | MIR camera and spec.
for Kiso Schmitt 1.0-m | KWFC | Wide field CCD imager
for KyotoSangyo-U 1.3-m | WINERED | NIR high resolution spec.
on miniTAO 1.0-m | ANIR | NIR camera
 | MAX38 | MIR camera
on Kiso Schmitt 1.0-m | 2kCCD | Wide field CCD imager
on Hokkaido-U 1.6-m | NICE | NIR mid resolution spec.
on Hiroshima-U 1.5-m | DMC | 15-bands CCD camera

## Slide 5: New technologies from the instrument projects
SWIMS
MIMIZUKU
KWFC
WINERED
MAX38
 CCD controller
 Filter changer with Robotic arm
 Immersion grating
 Metal mesh filter
 Moth-eye optics
 Cold Tip-Tilt
 Micro shutter

## Slide 6: Electrostatic drive type Micro shutter array
Micro shutter array
  Array of small shutters (0.1 to 1 mm size)
  Can open a shutter at an arbitrary position
  Use as a MOS slit  Simplify a MOS system
Array for JWST (Goddard) is closest to practical use
 scanning with magnets
 complex system
In this study, Electrostatic drive type has been developed.
King+05
Moseley+06
Motohara et al.

## Slide 7: Electrostatic drive type Micro shutter array
IoA, U-Tokyo + Institute of Industrial Science, U-Tokyo + NAOJ
Since 2004
With electrostatic force (>100V is necessary), not magnetic force
Simple addressing method
Succeeded in opening and closing shutters.
Next steps
  Structure to prevent light leak
  Stable behavior
  Larger format
1mm x 0.1mm

## Slide 8: Metal mesh filter
Wavelength (mm)
Transmittance
Miyata & Sako et al.
No good optical filters in 25 - 40 μm
  No transparent material in 25 – 40 μm
  × Multi-layer interference method
  In this study, MIR filters without transparent material have been developed.
Metal mesh filter
  Thin metal film with hole array
  Band-pass profile (R~10)
  Peak transmittance of ~100%
  Surface Plasmon-Polariton (SPP) effect
g
a
t ~ λ/10
λ

## Slide 9: Metal mesh filter
SEM image
Wavelength (mm)
Transmittance
29.5 μm pitch cross pattern
φ10mm
stacking 4 filters
Transmittance
↓ < 0.01%
300K
4K
measurements
R ~ 17
IoA, U-Tokyo + NTT-Advanced Technology + JAXA & NAOJ
Since 2006.
FDTD simulation & Photolithography fabrication
Succeeded in obtaining a peak trans. of > 90% and R~10
Blocking ratio of < 0.01% by stacking 4 filters
used in miniTAO/MAX38.
Next steps  Increase in Strength, Larger aperture

## Slide 10: Silicon Moth-eye
Sako & Miyata et al.
No good optical substrate in 25 - 40 μm
Silicon is one of the few potential candidates
Problem
・ High refractive index (n~ 3.4)
   High reflection loss (30% on one surface)
・ AR-coating is not available
  (the same reason of filters)
In this study, AR surfaces without multilayer interference have been developed.
Moth eye anti-reflection structure
  Sub-wavelength scale structure
  Broadband Anti-reflection effect
  Single material
Compound eye of Moth
20μm
1μm
Pillar structures with a pitch of 0.5 – 1μm on the surface of one eye

## Slide 11: Silicon Moth-eye
IoA, U-Tokyo + NTT-Advanced Technology + JAXA & KAKENHI
Since 2009
RCWA simulation & Photolithography and RIE fabrication
Succeeded in obtaining a trans. of 98% in 25 - 40μm on one surface.
Next step
  Both side, Moth-eye on Lens, Grism, and window, and for NIR.
- circular cone
- 60°adjacent
- pitch 5μm
- length 20μm
SEM images
Overview
10 x 10mm
Visible image
Results (measurement)
Design for MIR
Fabricated Silicon Moth-eye
10 20 30 40 50 60 70
1
0.9
0.8
0.7
0.6
Wavelength (μm)
Transmittance
100%
95%

## Slide 12: Cold Tip-Tilt Mirror
Nakamura et al.
Cryogenic opt-mechatronics is a key technology in TMT and SPICA era
  Expand the capability of infrared instruments
High stability and low power are needed
In this study, cryogenic tip-tilt (chopper) mirror for MIR observations has been developed.
Cold tip-tilt (chopper) system
   No need tip-tilt motion of 2ndary mirror
   Enables tip-tilt observations in space
  (to remove fast vibration generated by refrigerators)
MIR observation with chopping techniques
Typical chopping Freq. is
1 – 10Hz
Tip-tilt
2ndary
Cold
Tip-tilt
mirror
Cryogenic dewar

## Slide 13: Cold Tip-Tilt Mirror
IoA, U-Tokyo + Fuji ceramics + JAXA & KAKENHI
Since 2005.
Cryogenic piezo actuators were developed .
Stroke is extended by a factor of 2.7 at 7K
Succeeded in driving the chopper with
max 5 Hz and 15“ amplitude, and < 100mW at < 20K.
Used in miniTAO/MAX38
Next step  2-axis type, larger amplitude, faster feedback
Driving test of new piezos
Overview of Cold Tip-Tilt system
Observation image
A-beam
B-beam

## Slide 14
New CCD controller
No suitable controller for 1 – 8 CCDs system
Almost projects driven by University need small-mid sized system, not larger like HSC.
In this study, new CCD controller for small-med sized system (KAC: Kiso array controller) has been developed.
Kiso wide field camera (KWFC)
  Next generation open-use instrument on Kiso 1m telescope
  Wide F.O.V. (2deg x 2deg)
  8CCDs of 2k x 4k pixels
  4 SITe and 4MIT CCDs from NAOJ
  Opened in Apr. 2012
Sako et al.
2deg x 2deg 2010/12
KWFC camera
First light image

## Slide 15
New CCD controller
IoA, U-Tokyo + Several Universities and Institute in Japan (Hokkaido-U, Kyoto-U, AoyamaGakuin-U, and JAXA) + NAOJ
Since 2009
Succeeded in taking astronomical images with Kiso/KWFC
Welcome participation of this project
Development plan
  Redesign the analog circuit for Hamamatsu CCDs (2011/1-8)
  Installed into
   Spectrometer developed by
  Hokkaido-U and Kobe-U
   Kyoto 3D instrument for Subaru
   Test systems for Infrared and
  X-ray satellites
KAC analog boards for 8 CCDs

## Slide 16
Filter exchanger with Robotic arm
IoA, U-Tokyo + Mitsubishi electronics system & service + Sumitomo foundation
Since 2010
Filter exchanger is set at the prime focus of KISO Schmitt telescope
Uses an industrial robotic arm
Stores 16 filters (158 x 158 x 15mm) in the magazine box
Realizes a compact and lightweight system
Put an unique ideas to practical use
The arm and the magazines are placed on a framework of the telescope. The arm is evacuated outside of a beam in observations.
KWFC camera
Holder
(focal plane)
Filter Magazines
KWFC
Inside the Schmidt telescope
from the primary side
Filter exchanger
to be put here

## Slide 17
Immersion grating for NIR
Immersion grating
A sort of reflection type grating
Diffraction side is filled with ‘n’
Resolution and Physical size of spectrometer
High resolution spectroscopy with Large telescope
  a size of optics ∝ resolution
   large and heavy instrument  high cost
Immersion grating with large ‘n’ can downsize the optics
   In this study, immersion gratings for NIR have been developed.
Ikeda and Kobayashi et al.
φ ∝ R・D/n
φ : beam size
D : diameter of prime mirror
R : spectral resolution
n
θ

## Slide 18: Immersion grating for NIR
IoA, U-Tokyo + Photocoding + KyotoSangyo-U + NTT-Advanced Technology +Lawrence Livermore National Laboratory + JAXA & NAOJ
Since 2005
Two types of substrate : ZnSe (broad band), Silicon (high n)
Fabrication processes of grooves
ZnSe  nano precision fly-cutting technique (LLNL)
Silicon  anisotropic etching + photolithography (NTT-AT)
Succeeded in making high quality grooves with both methods
Next steps: improve diffraction efficiency and assemble the elements
Grooves on ZnSe
Grooves on Silicon
Silicon immersion grating
Silicon prism
Silicon grating
Optical
contact
Au

## Slide 19: Basic developments expand community and build a strong foundation
U-tokyo
Hongo
IoA
Lab A
Lab B
Company
Company
Company
Company
University
Institute
University
Company
Company
Company
Company
NAOJ
JAXA
University

## Slide 20: Universities are highly-responsive
U-tokyo
Hongo
IoA
Lab A
Lab B
Company
Company
Company
Company
University
Institute
University
Company
Company
Company
Company
NAOJ
JAXA
University
While energy sources are present,
the responses are continued.
Continuous and widespread supports
to the basic developments are important.

## Slide 21: Summary
U-tokyo
Hongo
IoA
Lab A
Lab B
Company
Company
Company
Company
University
Institute
University
Company
Company
Company
Company
NAOJ
JAXA
University
U-Tokyo has developed several new basic technologies in promoting mid-small sized instrument projects.
The basic developments have expanded the community on Japanese astronomy.
Continuous and widespread supports to the basic development are important to build a strong foundation toward TMT era.
While energy sources are present, responses between Universities are continued.