## Slide 1: SWIMS A New NIR MOS Spectrograph for TAO 6.5m Telescope
K. Motohara, M. Konishi, K. Tateuchi, N. Mitani, T. Aoki, K. Asano, M. Doi, T. Handa, K. Kawara, K. Kohno, S. Koshida, T. Minezaki,
T. Miyata, T. Nakamura, S. Sako, T. Soyano, M. Tanaka, T. Tanabe, K. Tarusawa, and Y. Yoshii

## Slide 2: TAO The University of Tokyo Atacama Observatory Project
Construct an infrared-optimized 6.5m telescope at the world’s highest site of 5650m(18000ft) altitude, Co. Chajnantor at Atacama desert, Chile
Current status:
  Installed a 1m telescope (called miniTAO), and started observations in the near- to mid infrared

## Slide 3: Advantage of Co. Chajnantor
Photometric nights > 60%, / usable >80% (Miyata+08)
Median Seeing 0.7” @ V-band (KM+08)
High Transmittance by low pressure (<0.5atm) + dry climate <= PWV 0.5mm (25%tile) (1mm@MKO)
Excellent observational condition in
both NIR(1-2.5mm) and MIR (5-40mm)
Atmospheric
Transmittance

## Slide 4: SWIMS Simultaneous-color Wide-field Imager and Multi-object Spectrograph
NIR Spectrograph for TAO 6.5m
  Wide-Field (9.6’ f FoV on TAO)
  MOS Spectrograph
  2-band simultaneous Imaging/Spectroscopy : 0.9-1.4 and 1.4-2.5mm
  R~1000 (4pix/0.52”slit)
Funded as a part of “Economy Stimulus Budget ”, 2009-2010
2.0m

## Slide 5: Science with SWIMS Galaxy Redshift Surevey
High transmittance at TAO site : Ideal for the redshift survey in the infrared
Full 0.9-2.5mm spectra can be obtained simultaneously : precise continuum / line ratio measurement possible
Simultaneous Hi-z Narrow-band Imaging (e.g. Ha/OIII, Hb/OII)

## Slide 6: Science with SWIMS New Window for Paa
Hydrogen Paa line (1.8751mm) available
  Strongest Hydrogen Line in NIR
  Good probe in dusty environment

## Slide 7: Paa Imaging with ANIR at Co. Chajnantor
Galactic Center (Sgr A*)
Starburst Galaxies IC4686/4687

## Slide 8: SWIMS Dewar Layout
Configuration on the Cassegrain Focus of
Subaru Telescope
Main Dewar
MOS Exchanger Unit
Optics
Unit
MOS
Slit Plate

## Slide 9: SWIMS Optics (Design/Fabrication : Optcraft)
Filter Wheels
For BBFs &
DIspersers
Filter Wheels
For NBFs
NBFs are placed in
Converging light
Dichroic Mirror
Blue Channel
(l = 0.9-1.4 mm)
Red Channel
(l = 1.4-2.5 mm)
Split collimated beam using a Dichroic Mirror(DM) at 1.4mm
Final F-ratio=4.8 : 0.13”/pix
Independent filter wheels for NBFs to avoid wavelength offset
Each focal plane is covered by 2 H2RGs
f 7.2’

Future
6.6 x 3.3’
1600mm
230mmf

## Slide 10: SWIMS on Subaru/Cassegrain
TAO 6.5m not available before 2016
First science with Subaru
Collimator design optimized for Subaru (Re-optimized to TAO by changing the collimator unit)
FoV of 6.6’ x 3.3’ (MOIRCS : 7’x4’)
0.10”/pix

## Slide 11: Performance of Optics (Subaru Design)
Blue Channel
Red Channel

## Slide 12: Focal Plane Arrays
8 HAWAII2 RGs / 2.5mm cutoff => Currently only 4 procured/delivered
SIDECAR ASICs for readout
Covers central 6.6’x3.3’ FoV@Subaru
0.1”/pix sampling
#196
#206
#208
#191
Dark Current < 0.005e-/s

## Slide 13: MOS Slit Plate Exchanger (Design/Fabrication : Sentencia)
Mask Catcher Unit (Robo-hand)
Not Shown here
Gate Valve
Collimator Unit
MOS Slit Masks
Based on the design of MOIRCS
  Turret-type mask stocker
  Robotic mask exchanger
~2.3m

## Slide 14: MOS Slit Unit / Holder
Maximum # of mask slit : 20
New design with high reliability
  Magnet – latch (Both at the focus and the stock)
  Operative even at the TAO Nasmyth focus
  Curved mask to adjust focal plane curvature
Prototype Mask Holder
250mm
210mm
Neodyium Magnets

## Slide 15: Schedule
2010/Nov : Array #1, #2 delivery
2011/Jan : Closing design phase
2011/Jan : Array #3, #4 delivery
2011/Jan : Dichroic mirror delivery
2011/Mar : Completion of a new laboratory building
2011/Mar: Delivery of the dewar, MOS, optics componetns
2011/Q2-2012/Q2 : Assembly, adjustment, etc…
2012/Q3 or later : Transport to Subaru, setup
2013/Q1 : First Light at Subaru ?

## Slide 17: New Building at Mitaka
Wii be completed in mid-March

## Slide 18: Mask Catcher Unit

## Slide 19: Atmospheric Transmittance
5600m
PWV=0.5mm
4200m
PWV=1.0mm
2600m
PWV=6.0mm

## Slide 20: Dichroic Mirror