## Slide 1: Expanded Ground-Based Kepler Array: Phase 1
Danielle Doughty
Alex Felli
Craig McNabb
Kelsey Miller
Iain Pearson
Steph Sallum
Nick Thelin

## Slide 2: Mission Objective
Multi-phase approach
  Phase I: Detection
  Phase II: Imaging
Detection of Earth-size planet transits
Full sky coverage
Ground based array
Future direct imaging of planet candidates

## Slide 3: Current Transit Mission Comparison: Kepler
Space based telescope
Aperture: 0.95 m
FOV2: 105 deg2
  Dimmest mag: 12
  Exposure time: 6.5 sec
  Cadence: 1 min, 30 min, 5 hrs
  Can detect Earth-like transit:
    Around G2V star
    @ 4sigma
    6.5 hr total integration time
http://kepler.nasa.gov/Mission/QuickGuide/MissionDesign/PhotometerAndSpacecraft/

## Slide 4: Current Transit Mission Comparison: Kepler
CCD
  Array of 42 CCDs
  Each 50x25 mm
  Each with 2200x1024 pixels
  Read out ever 6 seconds
  Defocused to 10 arcsec
  Data downlink: 1/month
  Planet candidates to date: 2740
  Eclipsing binaries (false positives): 2165
  Confirmed planets: 114
http://kepler.nasa.gov/Mission/QuickGuide/MissionDesign/PhotometerAndSpacecraft/

## Slide 5: Design Process: Science Goals
Phase 1:
  Full sky coverage
  Target stellar magnitude: 12
  Sensitivity: 10PPM
Phase 2:
  Direct imaging of exoplanet candidates

## Slide 6: Design Process: Science Goals
Sensitivity Calculations:
  Calculate by exposure time the highest magnitude at which 10 PPM sensitivity is achievable
  Define sensitivity as the change (in PPM) corresponding to 3σ
  Assume noise sources are Poisson & sky only
    F* = F0λ × 2.515-m × λ in photons m-2 s-1
    S* = F* × (πD2) × Δt in photons
    Same formulae for Fsky and Ssky assuming background of 21 mag arcsec-2
    N = √(S* + Ssky)

## Slide 7: Design Process: Science Goals
4 m
8.4 m
We chose an 8.4 m aperture with a 10 minute exposure time.
Target Star Magnitude vs. Exposure Time

## Slide 8: Design Process: Science Goals
With 50% detector efficiency
With a perfect detector

## Slide 9: Design Process: Science Goals

## Slide 10: Design Process: Science Goals
Phase 1:
  Transit period > 3hrs
  Orbital period < 2 months

## Slide 11: Design Process: Ground vs Space
Ground
  Pros
    Easy to update
    Lasts for many years
    No need to worry about other orbiting debris hitting structure
    No need for self contained energy source or communications gear
    Cheaper!!!
      Keck (10m diameter $100M in 1992)
  Cons
    Looking through atmosphere
      Reduction in resolution
      Reduction in usable wavelengths
    Can only operate at night
    The Earth ROTATES!
Notes: danielle

## Slide 12: Design Process: Ground vs Space
Space
  Pros
    Do not have to deal with atmosphere
      Better resolution
      Able to use full spectrum
  Cons
    Will only run for a few years
    Technology is out of date by launch date
    Downlinking data is expensive
    Cannot be updated after launch due to expenses and accessibility
    Testing of any new technology
    Expensive!!!
      Kepler $550M first 3 years
        Building from Ball Aerospace ($236M)
        $18M each following year (till 2016)

## Slide 13: Design Process: Telescope Specs
Mirror design
  Schmidt Telescope Design
    Reduce Coma
  F/1.19
  10° FOV
  8.4m Diamater
  -20m Radius Of Curvature

## Slide 14: Design Process: Telescope Specs
Minimizing Aberrations
  Spherical Wave fronts With Radius of Curvature of -10 meters
  Induces Spherical Aberration
    Eliminated by curving CCD Array

## Slide 15: Design Process: Telescope Specs
CCD Design
  1.7m Diameter
  373.2 MegaPixel Array
  -10m Radius of Curvature
    Related to Focal Length of Telescope

## Slide 16
Minimizing Aberrations - Coma
  Coma Present Due To Off Axis Rays
    Eliminated by placing a stop at the Radius Of Curvature Of The Mirror
  Further Reduce Aberrations By Aspheric Corrector Plate
Design Process: Telescope Specs

## Slide 17: Telescope Specs: How Well Does It Perform?
On Axis Spot Size of 5um
Off Axis Spot Size of 1.2mm
Only 0.5 Waves of Spherical Aberration
M=7000x
Object Entering Telescope
Conjugate Image Formed On CCD Array

## Slide 18
Design Process: Thermal Properites

## Slide 19
Design Process: Mechanical Properites

## Slide 20
Design Process: Telescope Specs

## Slide 21
Design Process: Active Optics
Effects of Shape change for one individual actuator exerting 1N of force on a 6.5m honeycomb mirror. The surface contours are shown at 5nm.
Actively shapes a telescope's mirrors to prevent deformation due to external influences such as wind, temperature, mechanical stress.

## Slide 22
Design Process: Active Optics Design
  Three zones of supports to control active optics.
  Enables Tip, tilt, and piston.
  Hydraulic system.
  Actuators connected to mirror by puck bonding at honeycomb intersections.
  Each actuator has a three point load spreader.
  262 Pucks bonded.

## Slide 23
Design Process: Active Optics Design
  Three zones of supports to control active optics.
  Enables Tip, tilt, and piston.
  Hydraulic system.
  Actuators connected to mirror by puck bonding at honeycomb intersections.
  Each actuator has a three point load spreader.
VLT Primary Support

## Slide 24
Design Process: Telescope Specs

## Slide 25
Design Process: Telescope Specs

## Slide 26: Design Process: Main Idea
Divide the sky into subregions
Continually scan over a particular subregion, switching between telescopes as the Earth rotates
After a given amount of time, move to a new subregion
We can look at 2 subregions at a time (Northern and Southern hemisphere)

## Slide 27
Design Process: Number of Telescopes
Let θ be the minimum angle above the horizon we can observe
We need to be able to see the same portion of sky for all 24 of the day
Absolute minimum number of telescopes:

## Slide 28
Put N telescopes in each hemisphere
Required longitude separation Δ between telescope locations:
Design Process: Number of Telescopes

## Slide 29
Design Process: How much of the sky will we be able to see?
Let β1n, β2n, …, βNn be the magnitudes of the latitudes of the N telescopes in the Northern hemisphere
Assume all β < 90°-θ
Let βminn = min{β1n, β2n, …, βNn}
Then define βs’s and βmins in the same way for the Southern hemisphere

## Slide 30
Design Process: How much of the sky will we be able to see?
If βminn, βmins > θ, then we will be able to see the full sky (4π sr)
If βminn, βmins < θ, then the fraction of sky we will see is

## Slide 31
Design Process: How much of the sky will we be able to see?
Since our FOV is circular, we will look at circular patches of sky
If we don’t overlap, then highest packing density is hexagonal
So we will cover 90.9% of the sky

## Slide 32
Texp = exposure time
Ttransit = time duration of fastest transit we want to observe
P = largest orbital period of planets we want to detect
Ns = number of data samples required during the duration of the fastest transit
Ntransits = number of transits required to say there’s a planet
Design Process: How much of the sky will we be able to see?

## Slide 33
Design Process: Main Idea

## Slide 34
Design Process: Some assumptions
Telescopes can observe as low as 20 degrees above the horizon
Each portion of the sky will be visible for at least 6 months
3 transit detections are required to say there’s a planet there
Transit duration is about 3 hours
We need 3 data points over the duration of a transit

## Slide 35
Design Process: The result
To view the entire sky, we need 3 telescopes in each hemisphere, with longitudes separated by less than 140°, and latitude magnitudes greater than 20°
21 subregions in each hemisphere
Scan over 6 FOVs in each subregion
Total project duration will be 11 years

## Slide 36
Design Process: We should then be able to find 90% of planets with:
Host star magnitude 12 or lower
Orbit aligned between host star and Earth
Orbital period less than 2 months
Transit time of at least 3 hours

## Slide 37
Design Process: Telescope Locations (Northern Hemisphere)
Maui, Hawaii
  20.42N, 156.15W, 3058m
La Palma, Canary Islands, Spain
  28.46N, 17.53W, 2400m
Lijiang, China
  26.52N, 100.14E, 3250m

## Slide 38
Design Process: Telescope Locations (Southern Hemisphere)
Cerro Pachon, Chile
  30.20S, 70.59W, 2737m
Coonabarabran, Australia
  31.17S, 149.04E, 1165m
Sutherland, South Africa
  32.23S, 20.49E, 1759m

## Slide 39
Design Process: Map

## Slide 40: Data Processing: Storage
Each raw image taken will produce an image size that corresponds to approximately 373.2MP
Assuming an image is taken every 10 minutes and eight hours of night, we will produce approximately 18GB of data per night per site
Each month we will have 540GB per site per month
Each image is scanned for known stars, this allows the image to be calibrated photometrically and astronomically.

## Slide 41: Data Processing: Structures
Three Data Structures
  Infrastructure Layer
    Consists of computing, storage, and networking hardware and software
  Middleware Layer
    Handles processing, data access, user interface, and system operations services
  Applications Layer
    Comprised of data pipelines and science data archives

## Slide 42: Data Processing: Data Flow
Telescope
CSV
Files
Image Processing Pipeline (IPP)
CSV
Files
Load Workflow
Load Workflow
Load DB
Load DB
Cold Slice DB 1
Cold Slice DB 2
WarmSlice DB 1
WarmSlice DB 2
Merge Workflow
Merge Workflow
Hot Slice DB 2
Hot Slice DB 1
Flip Workflow
Flip Workflow
MainDB Distributed View
MainDB
Distributed View
CASJobs
Query Service
MyDB
MyDB
← Behind the Cloud|| User facing services →
Validation Exception
Notification
Data Valet Workflows
Data Consumer
Queries & Workflows
Data flows in one direction→, except for error recovery
Slice Fault Recover Workflow
Data Creators
Astronomers
(Data Consumers)
Admin & Load-Merge Machines
Production Machines

## Slide 43: Data Processing: Transit Detection
Light curve generation
  Harder than Kepler due to sky background
  Compare target star to mean of all other stars in the field
    Minimizes chance of having a variable/transiting comparison star contaminating target light curve

## Slide 44: Data Processing: False Positives
False positives
  Undiluted eclipsing binaries (strong radial velocity variations not compatible with planetary scenarios) with a low mass stellar companion
  Diluted eclipsing binaries (‘blends’) whose eclipse depth is diluted with the target flux (by another star in the system) and can therefore mimic a planetary transit
  For Kepler an overall FPP of less than 10% for 90% of the candidates with a median value close to 5%.
Notes: KELSEY

## Slide 45: Data Processing: False Positives
Confirmation methods
  Radial Velocity
    Can be done with other, smaller ground based telescopes (has been done by SOPHIE spectrograph mounted on the 1.93-m telescope at the Observatoire de Haute-Provence for Kepler candidates)
    Has been done by performing weighted cross-correlation with a numerical G2 mask
  Transit time variation technique
    exclude outliers and transit times with unusually large uncertainties
    reject any transit times for which the measurement uncertainty exceeds twice the median of the transit time uncertainties
Notes: KELSEY: Radial velocity measurements: obtained by performing weighted cross-correlation with a numerical G2 mask
Transit time variation:linear ephemeris (L2) calculated after cleaning the transit times to exclude outliers and transit times with unusually large uncertainties. Speciﬁcally, we reject any transit times with an absolute deviation from the linear2 Ford et al.
ephemeris exceeding four times the median absolute deviation of transit times from the ﬁrst linear ephemeris (L1). We also reject any transit times for which the measurement uncertainty exceeds twice the median of the published transit time uncertainties. We record the median timing uncertainty for the remaining NT T transit times
(σT T). Then, we calculated an updated the best-ﬁt linear ephemeris (L2) using the cleaned transit times. We report the epoch (Elin) and period (Plin) of the updated linear ephemeris (L2) in the electronic table.
We consider a small p-value as indicating that a transit timing data set is worthy of further investigation

## Slide 46: Expanded Ground-Based Kepler Array vs Kepler
EGBKA
  6 telescope array
  Ground based
  Visible wavelengths
  Sensitivity (PPM): 10
  Dimmest visible mag: 12
  Exposure time: 600 sec
  Cadence: 60 min
  f/#: 1.19
  Primary D: 8.4 m
  Corrector plate D: 8.4 m
  F: 10 meter
  CCD : 1.7m
  FOV2: 95 deg2
  90.69% full sky coverage
  Phase 1 duration: ~ 11 yrs
Kepler
  Single aperture
  Space based
  Visible wavelengths
  Sensitivity (PPM): 441 (SC) 80.5 (LC) 25.4 (hr C)
  Dimmest visible mag: 12 (catalogued)
  Exposure time: 6.5 sec
  Cadence: 1 min, 30 min, 5 hrs
  f/#: 1
  Primary D: 1.4 meter
  Corrector plate D: 0.95 m
  F: 1.4 meter
  CCD : 0.78m2
  FOV2: 105 deg2
  0.25% full sky coverage
  Mission duration: >7.5 years
Notes: KELSEY

## Slide 47: Revisions After This Slide
Notes: KELSEY

## Slide 48: EGBKA Re-Design
Telescope & CCD design
  Schmidt design
  Segmented mirror
  Segmented corrector plate 30 ft above primary
  f/1.19
  Diameter: 4 meters
  λ/D: 0.025 arcsec
  Focal length: 4.76 meters
  Plate scale: 43.33 arcsec/mm
  FOV: 10 degrees
  Pixel size: 0.16 micron
  CCD size: 0.83 meters
  2.5*1013 pixels
Layout
  6 telescope array
  3 locations around the equator
  2 telescopes per location
Notes: KELSEY

## Slide 49: EGBKA Re-Design
Observations
  Only galactic plane (30deg x 180deg)
    8.3% full sky
    Pro – high star density
    Con – potentially giving up closer star systems
  Exposure time: 3 min
Notes: KELSEY

## Slide 50: Revised Sensitivity Calculations
  Calculate by exposure time the highest magnitude at which 10 PPM & 100 PPM sensitivity are achievable
  Define sensitivity as the change (in PPM) corresponding to 3σ
  Assume noise sources are Poisson, sky, and scintillation
    F* = F0λ × 2.515-m × λ in photons m-2 s-1
    S* = F* × (πD2) × Δt in photons
    Same formulae for Fsky and Ssky assuming background of 21 mag arcsec-2
    σscin = 0.003 D-2/3 T-1/2 (Kornilov et al. 2012)
    N = √(S* + Ssky+σscin2)
Notes: KELSEY

## Slide 51: 10 PPM
Notes: KELSEY

## Slide 52: 100 PPM
Notes: KELSEY

## Slide 53: 4 Meter Aperture 3 Minute Exposure Time
Assumes 50% detector efficiency.
Notes: KELSEY

## Slide 54
Possible New Telescope Design
Corrector plate now has a smaller diameter than mirror
  Mirror Diameter = 4 meters
  Corrector Plate Diameter = 2.63 meters
  This gives the CCD have a diameter of 851mm
    Much more realistic!